## Slide 1
AUTOMATED GREENHOUSE
2550305M-FRASER MCLELLAN

## Slide 2
Contents
  1. Why
  2. Food imports
  3. Method
  4. Site
  5. Greenhouse
  6. Assumptions
  7. External conditions
  8. Heat transfer
  9. Greenhouse Temperatures
  10. Heat pump
  11. Refrigerant
  12. Heat pump analysis
  13. Simulation process
  14. Power supply
  15. Impact
16-22. Appendices

## Slide 3
Why?
LSHTM. (n.d.). One third of UK fruit and vegetables are imported from climate-vulnerable countries – and this is on the rise. [online] Available at: https://www.lshtm.ac.uk/newsevents/news/2020/one-third-uk-fruit-and-vegetables-are-imported-climate-vulnerable-countries.
‌
Notes: With temperatures around the world risnig, many sub-saharan and equatorial regions will become non-arable. Many of the crops we import regions where we grow, soyabean, avacados and many of the fruits and vegetables we in our society cook and eat every day. If we are going to continue without change in our diets, we most change our production methods.

## Slide 4
FOOD IMPORTS
GOV.UK. (n.d.). Horticulture statistics - 2022. [online] Available at: https://www.gov.uk/government/statistics/latest-horticulture-statistics/horticulture-statistics-2022.
‌
Quantity (tonnes)
Notes: As a country we currently import ? amount of fruit and veg on an annual basis. This results in a large carbon footprint ? . however this can be changed if we were able to replicate the environment in the UK and massively cut down carbon emmissions from transport, and deforestation. The only question is how do we do so sustainably. Currently 71% of uk land used for agriculture. Much of that is livestock cultivation. food and drink inflatoin as of last year was at 18%. With rising prices and running out of space. tThere must be a way to become self sufficient in fruit and vegetable production.
32% of our imports come from moderately to highly vulnerable locatoins. 2020, 44% vegetables imported
84% for fruits.

## Slide 5
THE METHOD
Location & Greenhouse
Heat pump design
Heat transfer
Results
Notes: To present the study we will follow this process. first the initial design parameters of the greenhous.
secondly the external environments effects on the greenhous.
followed by the heat pumps contributions to maintaining the required temperature.
And finally the overall effects and feasibility.

## Slide 6
THE SITE
Notes: The site chosen for the greenhouse was close to Chelmsford, I'm not sure any of you will of been or heard of it but it is a small town on the coast north east of london. It sits near the river Crouch which would supply the water source heat pump, along with year round temperature data going back to 200?. The daily highs and lows of both ground and air temp were extracted and manipulated by the equation seen on screen to form a day night cycle. This data is essential in calculating the heat losses due to the external surroundings as you will see.

## Slide 7
THE GREENHOUSE
Notes: The greenhouse itself is 400m^2 in area with a height of 5m this is on the large end of the industrial scale. This is to assume replicating the imports from abroad would take multiple (how many) greenhouses of this size to match the demand. The wall material chosen is transparent polycarbonate panels. it's thermal conduction coefficient is 0.23, representing good insulating properties while allowing sunlight in to help heat the greenhouse in the summer. This material is already being substitued in many countries for the more expensive glass. The floor is currently made of 15cm concrete concrete slabs. posessing a conduction coefficient of 0.87.

## Slide 8
SIMULATION: UML DIAGRAM
Temperature generation
Heat transfer calculator
Internal temp>= 18
Else
Heat transfer calculator
with Qc value
Heat pump calculator
Data reading
Refrigerant properties extraction
Qc = 0
Heat pump off

## Slide 9
ASSUMPTIONS
Greenhouse
    Heat dissipates evenly
    Constant pressure
    Air flow is evenly distributed, air density distribution is uniform
    PVC is in steady state
    100% of solar kWh absorbed by panels
Heat pump
    Condenser losses are negligible
    Refrigerant is saturated
    Compression is isentropic
Notes: through connections between panels, and ground
within the greenhouse
with no internal heat sources and uniform material properties across panel.
at evaporator, condenser and flashtank

## Slide 10
EXTERNAL CONDITIONS
www.chelmervillage-weather.co.uk. (n.d.). Chelmsford Weather Station - Soil Temperature. [online] Available at: https://www.chelmervillage-weather.co.uk/wxsoiltempdetail.php? [Accessed 14 Mar. 2024].
‌

## Slide 11
HEAT TRANSFER
Notes: Moving onto the heat transfer calculations. the heat lost through the walls was calculated using the equation shown on screen.
Next the sunlight energy was provided in kWh which was converted to W for calculation reasons. and finally a total was found by summing these values which was used to calculate the new internal temperature based off of the heat losses/gains to the external environment. as seen on screen.

## Slide 12
INTERNAL TEMPERATURES
Notes: This is the result. following the calculations on the previous slide, the unregulated internal temperature over a 6 year period was plotted. This is the basis for the study. From these temperatures we can calculate the necessary heating requirements to maintain a pleasant environment for a given crop growth.

## Slide 13
THE HEAT PUMP
Notes: The heating element employed for this greenhouse was a multistage heat pump containing a flashtank intercooler. This was chosen for a variety reasons. first being the relatively low temperatures employed. with heating required to be 30 degrees. I will not walk you through each individual stage however the importance of the flashtank is due to the relatively low temperatures employed. it ensures that the refrigerant entering the subesquent stages is predominantly in the vapor phase. preventing dmage and encouraging stability. acting almost like a buffer against variations in the refrigerants composition.A flashtank intercooler operaitng heat pump was employed. This is due to the ability to operate at lare temperature differences, which occurs occure throughout the winter. Vital for year round productio

## Slide 14
REFRIGERANT: AMMONIA
Global Warming Potential: 0
Ozone Depletion Potential: 0
Specific heat capacity: 1343-9312 kg/kJ
A N I N T E R N A T I O N A L O R G A N I Z A T I O N ASHRAE Position Document on AMMONIA AS A REFRIGERANT. (n.d.). Available at: https://www.epa.gov/sites/default/files/documents/ASHRAE_PD_Ammonia_Refrigerant_2010_1.pdf.
‌

## Slide 15
HEATPUMP COMPARISON
Air source
  COP: 3.66
  kwh/annum: 159,000
Ground source
  COP: 3.7
  kwh/annum: 157,500
Water source
  COP: 3.91
  kwh/annum: 149,000

## Slide 16
POWER SUPPLY
Notes: 100kw
10M radius
produces enough with mean wind speed of 3.9m/s

## Slide 17
IMPACT
Blaauw, Sheldon and Broekman, Andre and Maina, James and JvdM Steyn, Wynand and Haddad, Wiam, Life Cycle Assessment of an Avocado: Grown in South Africa – Enjoyed in Europe. Available at SSRN: Add a little bit of body text or Add a little bit of body text
Notes: october-march, requires additional lighting.
1 avacado tree needs 171.73w/m^2
do not get that in november december january,, therefore extra lighting of maximum 90w/m^2 multiply by area of room, therefore 36kW of lighting, can be supplied by excess in turbine as max for compressor is 60kW

## Slide 18
THANK YOU

## Slide 19
Temp generation
Heat transfer
(With heat pump)
Heat Pump
APPENDIX: EQUATIONS

## Slide 20
APPENDIX: AMMONIA EXTRACTION
Extract row from saturated properties (vapor)
Extract row from saturated properties (liquid)
Extract row from saturated properties (vapor)
Stage 1:
Stage 2:
Stage 3:
Stage 4:
Stage 5:
Stage 6:
Stage 7:
Extract row from Superheated properties
Extract row from Superheated properties
https://web.iiar.org/membersonly/PDF/CO/databook_AppA.pdf
1
2
3
4
5
6
7
P (kPa)
h (kJ/kg)

## Slide 21
APPENDIX: RADIATOR

## Slide 22
APPENDIX: CONSTANTS
Air:
Turbine:
Radiator:
Nusselt number::

## Slide 23
APPENDIX: COMPRESSOR POWER

## Slide 24
APPENDIX: MASS FLOW RATES

## Slide 25
APPENDIX: UML
Temperature generation
Heat transfer calculator
Heat pump values
attributes:
h_1
h_2
h_3
h_4
h_5
h_6
h_7
operations:
M_2(Qc)
M_1(M_2)
W_c1(M_1,h_2,h_1)
W_c2(M_2,h_4,h_3)
Q_e(M_1,h_2,h_7)
COP(Qc,W_c1,W_c2)
for i in range (2190):
for k in range(24):
Time
Data reading
refrigerant property extraction
Condition
Heat transfer calculator
attributes:
i
k
Operations:
t = i +k/24
attributes:
df_saturated
df_superheated
dF_aitremp
df_soiltemp
df_sunlight
operation:
pd_read.csv(attributes)
attributes:
Tmax_a
Tmin_a
Tmax_g
Tmin_g
Tmax_w
Tmin_w
operations:
ground_temperature_variation(t)
external_temp_variation(t)
water_temp_variation(t)
attributes:
k(wall,ground)
A(wall,ground)
initial_internal_temperature
d(wall,ground)
m(air)
c(air)
transparency
operations:
Q_total(T_internal,external_temp,ground_temp, sunlight)
T_internal(Q_total)
if T_internal >= 18:
Else
attributes:
T_internal
m(air)
c(air)
operations:
Q_total(T_internal,external_temp,ground_temp, sunlight)
Q_c(T_internal,Q_total)
T_internal(Q_total,Q_c)
attributes:
df_saturated
df_superheated
dF_aitremp
df_soiltemp
T_1
P_values
h_values
s_values
T_values
operations:
extract_values(T_1, h_values, P_values, s_values, T_values)
Q_c = 0
T_internal = Heat_transfer_calculator.T_internal(Q_total)

## Slide 26
ADDITIONAL REFERENCES
https://www.geturbanleaf.com/blogs/fruit/growing-avocado-indoors#:~:text=In%20order%20to%20provide%20an,500%20%CE%BCmol%2Fm%C2%B2%2Fs.
conversion: https://www.waveformlighting.com/horticulture/convert-ppfd-to-lux-online-calculator